## Slide 1: Drive Your Server Like You Stole It
HOTSOS 2017
Andy Weiss & Kirby Sand

## Slide 2: Presentation Overview
Introduction
Problem Statement
Experiment Design and Results
Conclusions & Future Work
Acknowledgements

## Slide 3: Introduction
We work for Hewlett Packard in Corvallis Oregon
We are on a team that builds really big printers
Engineering Analytics
  Analytics on large datasets to provide insights to the engineering teams, the tiered support organization, and to the end customer.
    Failure mode detection
    Machine performance
    Fundamental engineering models
Our Data
  Raw sensor information
    temperature, pressure, speed, tension, vision system output, etc.
  Device status information
    Alarms, faults, compute system usage, etc.
  Production information
    Jobs, consumables, operator interactions, etc.
  The data is linked only by the device it came from and the timestamp.

## Slide 4: The Different Approaches to Tuning
The 3 R’s of query tuning
  Reduce
    Partition pruning, indexing, etc.
  Reuse
    Pre-Aggregation, Bind variables, SQL Plan Baselines, etc.
  Rev It Up!
    Use your resources
Sometimes you just have to crunch a lot of data…
  Monthly/Weekly/Nightly/Hourly Jobs
  Ad-hoc queries

## Slide 5: Why are we going to temp?
11.2.0.4
PGA 800GB
72 cores
16GB Temp
1.4GB PGA
19GB PGA
Same query with a manual sort area size
0 Temp

## Slide 6: Which also causes inefficient utilization of CPU

## Slide 7: Let’s set up a test … how hard can it be?
12.1
512G ram
16 cores
What we thought we knew
What we wanted to know
What we actually knew

## Slide 8: Experiment Overview (Representative Tables & Queries)
Parent/Child Analytics
  Tables
    PARENT_TABLE_V1
      50M Rows, 1GB
    CHILD_TABLE_V1
      5B rows, 100GB
  Standard Analytic Functions
    Avg/Sum/Count
Windowing Functions
  Tables
    LEAD_LAG_TEST_V1
      2.4B rows, 60GB
  Windowing Functions
    Lead/Lag finding changes
Single Table Analytics
  Tables
    CAPSTONE_PARALLEL_TEST_V1
      32M rows, 7GB
  Standard Analytic Functions
    Avg/Sum/Count
Filter Parent/Child Join
  Tables
    PARENT_TABLE_V1
      50M Rows, 1GB
    CHILD_TABLE_V1
      5B rows, 100GB
  Filter with WHERE clause

## Slide 9: PGA Overview
How do we measure it?
V$PGASTAT
V$PROCESS
V$SQL_WORKAREA_ACTIVE
V$SQL_WORKAREA
Parameters
PGA_AGGREGATE_TARGET
WORK_AREA_SIZE_POLICY
*_AREA_SIZE

## Slide 10: PGA Sizing Calculations
_PGA_MAX_SIZE:
  max ( 200MB , min ( 2GB, 20% of PAT ))
_SMM_MAX_SIZE:
  min ( 20% of PAT, 50% of _PGA_MAX_SIZE )
_SMM_PX_MAX_SIZE:
  50% of PAT

## Slide 11: Experiment # 1: Tuning PGA
We manually set _pga_max_size
  ALTER SYSTEM SET “_PGA_MAX_SIZE” = 2G
  ALTER SYSTEM SET “_PGA_MAX_SIZE” = 4G
  ALTER SYSTEM SET “_PGA_MAX_SIZE” = 6G
We forced DOP with a hint
  /*+ PARALLEL(16) */
  /*+ PARALLEL(32) */
  /*+ PARALLEL(64) */
We forced buffer cache to be small
  512MB (no table fits)
We tracked resource usage
  Work Area Size (PGA and Temp)
    V$SQL_WORKAREA_ACTIVE
  Time (Run Time, CPU Time, IO Wait, DB Time)
Can we stop going to temp if we enable larger work areas?

## Slide 12: Experiment # 1: Tuning PGA
Biggest gains happen when we never go to temp.
  Approx. 1.3X improvement over default
How do we prevent TEMP?
  Really high DOP
    Not ideal, requires lots of CPU without a big improvement in run time.
  4G PGA_MAX_SIZE
    A more attractive approach. Allows us to use more PGA
    Somewhat scary since it’s an undocumented parameter
Default

## Slide 13: SGA Overview
Quick refresher on SGA memory structures
Areas of interest for us
Buffer Cache
In-Memory Column Store

## Slide 14: Automatic Big Table Caching
Parameters
PARALLEL_DEGREE_POLICY
DB_BIG_TABLE_CACHE_PERCENT_TARGET
_SMALL_TABLE_THRESHOLD
2% of buffer cache
How do we measure it?
V$BT_SCAN_CACHE
V$BT_SCAN_OBJ_TEMPS

## Slide 15: Experiment # 2: Big Table Caching
We manually set parallel degree policy
  ALTER SYSTEM SET PARALLEL_DEGREE_POLICY = MANUAL
  ALTER SYSTEM SET PARALLEL_DEGREE_POLICY = AUTO
We manually set Big Table cache percent target
  ALTER SYSTEM SET DB_BIG_TABLE_CACHE_PERCENT_TARGET = 10
  ALTER SYSTEM SET DB_BIG_TABLE_CACHE_PERCENT_TARGET = 50
  ALTER SYSTEM SET DB_BIG_TABLE_CACHE_PERCENT_TARGET = 90
We forced DOP with a hint
  /*+ PARALLEL(32) */
We forced PGA_MAX_SIZE
  ALTER SYSTEM SET “PGA_MAX_SIZE” = 4G
We made buffer cache big
  192GB
We tracked resource usage
  Time (Run Time, CPU Time, IO Wait, DB Time)
  BT Cache Object Status
    V$BT_SCAN_OBJ_TEMPS
Can we put tables into memory and eliminate or minimize IO?

## Slide 16: Experiment # 2: Big Table Caching
Policy = Manual
  Notice that as the cache percent target gets large, the queries slow significantly.
Policy = Auto
  As you increase the big table cache percent you get significant query speed improvements.
    2.6X speed improvement from the default
  However, you still have to go disk for some of the data.

## Slide 17: Experiment # 2: Big Table Caching
Notice that you appear to pay a penalty on the first run, but if your buffer cache is large enough you significantly improve the subsequent runs.
This isn’t ideal for something like a nightly job because those typically aren’t run more than once.
This might be a very nice solution for ad-hoc queries on large tables.

## Slide 18: In-Memory Column Store
Row Storage
Columnar Storage
Buffer Cache
IMCS
Parameters
INMEMORY_SIZE
How do we measure it?
V$IM_SEGMENTS
V$INMEMORY_AREA

## Slide 19: In-Memory Pools
1MB Pool
64KB Pool
SMU
SMU
SMU
SMU
SMU
SMU
SMU
SMU
SMU
SMU
SMU
SMU
Used to store actual data populated in columnar format
Subunits knows as In-Memory Compression Units (IMCU)
Column stores composed of 1MB extents
Data can be stored over one or more IMCU
1MB Pool Size = (0.8 * INMEMORY_SIZE)
Contains IMCU metadata and transactional information
Individual subunits known as Snapshot Metadata Units
64KB Pool Size = (0.2 * INMEMORY_SIZE)
v$inmemory_area
v$im_header
v$im_smu_head
V$im_segments
IMCU
IMCU
IMCU
Dynamic Performance Views

## Slide 20: Experiment # 3: In-Memory Column Store
We manually set…
  ALTER SYSTEM SET PARALLEL_DEGREE_POLICY = AUTO
  ALTER SYSTEM SET DB_CACHE_SIZE = 32G SCOPE=SPFILE
  ALTER SYSTEM SET INMEMORY_SIZE=192G SCOPE=SPFILE
  ALTER SYSTEM SET “PGA_MAX_SIZE” = 4G
We forced DOP with a hint
  /*+ PARALLEL(32) */
We forced tables to be InMemory
  ALTER TABLE [table name] INMEMORY MEMCOMPRESS FOR QUERY LOW PRIORITY CRITICAL
We waited for the table to fully populate In-Memory
  V$IM_SEGMENTS
We tracked resource usage
  Time (Run Time, CPU Time, IO Wait, DB Time)
How does IM compression change query speed?
How does compression option change object size in memory?

## Slide 21: Experiment # 3: In-Memory Column Store
“For Query Low” looks like a great choice
  Best performance (3.2X faster than going to disk)
  Decent compression (37% reduction)
For huge tables you could do “For Capacity High” so as not to use up all your In-Memory space.
  Still get a 2.6X improvement over going to disk

## Slide 22: Let’s Put It All Together…
Summary
  1.3X improvement from not going to temp
  3.4X improvement from also caching big tables
  4.2X improvement from using In-Memory
One Big Caveat…
  All experiments were run serially
    No competition for resources
    No other work being done on the system
    Not a real-world test case
So lets do a bunch of stuff all at once and see what happens…

## Slide 23: Experiment # 4: Statement Queuing
Queuing
No Queuing
Time
With Statement Queuing
  Queries are allocated the desired level or resources
  When PARALLEL_SERVERS_TARGET is surpassed, statements get queued
Without Statement Queuing
  Queries are all started as soon as they arrive, and CPU is downgraded causing some queries to run quickly, and some queries to run VERY slow.
  If you run without statement queuing and you include parallel hints in your query things can get ugly real quick.
Statements Downgraded

## Slide 24: Experiment # 4: Statement Queuing
Summary
  Statement queuing works like expected!
  Without queuing most jobs get massive downgrading and therefore lots of swap to temp
    Data was In-Memory for both sets of tests.
  With queuing each job gets the optimal resources it needs to execute
  Not shown:
    If you keep in parallel hints and have queuing turned off your queries will start to die with: ORA-04036: PGA memory used by the instance exceeds PGA_AGGREGATE_LIMIT

## Slide 25: Conclusions
Going to temp is bad
  Changing _PGA_MAX_SIZE allows us to increase our work area size without drastically increasing our DOP
Putting data into memory is good
  Big table caching is a good alternative if you don’t want to pay for the In-Memory option
  In-Memory column store is very performant

## Slide 26: Future Work
What we think we know
What we still want to learn
What we probably don’t fully understand

## Slide 27: Future Work
What happens with…
  Partitioning and parallel queries
  Table compression and parallel queries
  Indexing and In-Memory
  DML and In-Memory
  Resource Manager
Roll to production

## Slide 28: Acknowledgements
Hotsos!
OSU Computer Science Students
  Nathaniel Whitlock
  Nic Desilets
All the great Oracle Bloggers